## Slide 1
CSE224-Digital Logic Design Lab
Super Sensitive Intruder Alarm
PROJECT PRESENTATION
Mr. Shoumik Debnath
Lecturer,
Department of CSE
Daffodil International University
Presented to -
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 2
Super Sensitive Intruder Alarm
OUR TEAM
SUPAN ROY
ID: 232-15-716
ABDULLAH AL NOMAN
ID: 232-15-797
NUR SAYDA
ID: 232-15-437
MD. SHAHINUR KABIR ANTOR
ID: 232-15-159
SHAKIRA RAHMAN SIMI
ID: 232-15-723
Title
Team
Introduction
Circuit
Working
Applications
Conclusion
65_D1
Group4

## Slide 3
Introduction
🔸In today’s world, security is a major concern for homes, offices, and restricted areas.
🔸Our project focuses on building a cost-effective and highly sensitive intruder alarm system using basic
electronic components.
🔸The system uses infrared (IR) technology to detect motion or interruption in the IR beam.
🔸When someone blocks it, the alarm turns on, the system triggers a buzzer to alert about the intrusion.
🔸This kind of setup can help improve safety and awareness in any environment.
🔸This project is ideal for beginners and can be expanded for real-life security applications.
Super Sensitive Intruder Alarm
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 4
  NE555 Timer IC
  LM358 Operational Amplifier (Op-Amp)
  10K Preset/Variable resistor
  IR Transmitter
  IR Receiver
  Red LED
  Electrolytic Capacitor (10uF, 50V)
  Resistors: 10KΩ, 1KΩ, 100KΩ, 220Ω
  Buzzer
  Breadboard
  Connecting Wires Multiple
  5V Power Supply
Super Sensitive Intruder Alarm
Components Used
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 5
Fig. 1.1: Super Sensitive Intruder Alarm Circuit
Super Sensitive Intruder Alarm
Circuit Diagram
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 6
Fig. 1.2: Super Sensitive Intruder Alarm Circuit
Super Sensitive Intruder Alarm
Project Prototype
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 7
Working Principle
⚙️ 1. IR Transmitter Section
  IR LED emits invisible infrared light continuously.
  100Ω Resistor (R3) limits current to protect the IR LED.
  Light beam is aimed at the photodiode across the sensing area.
Super Sensitive Intruder Alarm
Fig. 2.1: IR Transmitter
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 8
Working Principle
Photodiode is in reverse bias: receives IR light and allows reverse current.
10kΩ Resistor (R4) works as a pull-down resistor, creating a voltage drop based on IR light intensity.
10kΩ Preset (RV1) sets a fixed reference voltage at LM358’s inverting input.
LM358 Op-Amp (Comparator) compares:
  Pin 3 (+): voltage from photodiode
  Pin 2 (–): reference from preset
When someone blocks IR beam:
  Photodiode voltage increases (Pin 3 > Pin 2)
  Comparator output (Pin 1) goes LOW to HIGH, triggering next stage
Super Sensitive Intruder Alarm
Title
Team
Introduction
Circuit
Working
Applications
Conclusion
Fig. 2.2: IR Receiver and Op-Amp (LM358)
👁️ 2. IR Receiver & Comparator Section

## Slide 9
Working Principle
NE555 Timer is configured in monostable mode.
Trigger Pin (Pin 2) is activated by LM358 output.
100kΩ Resistor (R1) and 10µF Capacitor (C1) define the ON-time.
On trigger:
  Pin 3 (Output) goes HIGH for a fixed duration.
  Timer resets automatically after time interval ends.
Super Sensitive Intruder Alarm
Fig. 2.3: 555 Timer IC
⏱️ 3. Monostable Timer Section (555 IC)
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 10
Working Principle
🔋 Power Supply:
  Whole circuit operates on +5V DC supply.
  All ICs and components are powered from this single source.
220Ω Resistor (R2) limits current to the Buzzer.
When 555 output is HIGH:
  Buzzer turns ON
  Produces alert sound indicating intrusion
Super Sensitive Intruder Alarm
Fig. 2.4: Buzzer Output
🔔 4. Output Section (Buzzer)
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 11
Super Sensitive Intruder Alarm
Applications & Future Improvements
✅ Applications:
🔹 Home Security Systems
Used at doors, windows, or hallways to detect unauthorized entry.
🔹 Bank & ATM Booths
Alerts security when someone enters during off-hours.
🔹 Warehouses & Storage Units
Protects valuable goods from theft by detecting movement.
🔹 School Labs or Server Rooms
Restricts access to sensitive areas when unsupervised.
🔹 Automatic Lighting Systems
Can be adapted to turn on lights when someone enters a room.
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 12
Super Sensitive Intruder Alarm
Applications & Future Improvements
🔄 Future Improvements:
🔸 Add SMS or Call Alert feature using GSM module.
🔸 Integrate with CCTV systems for real-time footage during intrusion.
🔸 Make it battery powered for portability and use during power cuts.
🔸 Add Wi-Fi or IoT support to control and monitor via smartphone.
🔸 Use motion sensors or camera-based detection for more accuracy.
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 13
Super Sensitive Intruder Alarm
🔹 Understanding Real-world Problem Solving
We learned how basic electronics can be applied to real-life security issues in a cost-effective way.
🔹 Circuit Design & Implementation
We gained hands-on experience building a working circuit using sensors, op-amps, and timers.
🔹 Sensor Technology
Understood how IR sensors work and how they can be used to detect objects or people non-contact.
🔹 Comparator and Timer Logic
Learned how a comparator (LM358) compares voltages and how a 555 timer functions in
monostable mode.
🔹 Troubleshooting & Debugging
Faced practical issues like incorrect wiring, loose connections, and fixed them to make the circuit
stable.
🎓 Learning Outcomes
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 14
Conclusion
GIGGLING PLATYPUS CO / TIMMERMAN INDUSTRIES / ALDENAIRE & PARTNERS
Super Sensitive Intruder Alarm
In this project, we successfully designed and implemented a Super Sensitive Intruder Alarm that can detect unauthorized entry using an infrared sensor system. The circuit provides a quick and reliable alert whenever the IR beam is interrupted, making it a practical solution for basic security needs. Through this work, we not only built a functional security system but also gained valuable knowledge about sensor technology, circuit design, and component integration. This project helped strengthen our teamwork and problem-solving abilities, and with future improvements, the system holds potential for real-world applications in homes, schools, and other secure areas.
Title
Team
Introduction
Circuit
Working
Applications
Conclusion

## Slide 15
Thank You!
FOR YOUR ATTENTION
Super Sensitive Intruder Alarm